## Slide 1: “1-D” MOOSE Project
Fuel pin dimensions listed
Assume reasonable values for thermal conductivities
  Can assume constant k
Outer cladding: 500 K
Mesh: 100x100
Solve temperature profile for:
  Steady-state: Volumetric/Areal heating rate:
  Q = 250 W/cm2
Solve for centerline temperature vs time
  Transient: Volumetric/Areal heating rate
    Q = 150*(1-EXP(-0.01*time))+250 for up to t=200
Fuel
Gap
Cladding
0.5 cm
0.1 cm
0.1 cm
1 cm

## Slide 2: 2-D MOOSE Project
Fuel pin dimensions listed
Assume reasonable values for thermal conductivities
  Can assume constant k
Utilize azial TCO, with reasonable flow rate, heat capacity, etc.
Solve temperature profile for:
  Steady-state: Volumetric/Areal heating rate: Q = 250 W/cm2
  @ z=0.25, z=0.5, z=1
Solve for centerline temperature vs time
  Transient: Volumetric/Areal heating rate
    Q = 150*(1-EXP(-0.01*time))+250 for up to t=200
  @ z=0.25, z=0.5, z=1
Find location of peak centerline temperature at SS, and at t=200 in transient
Fuel
Gap
Cladding
0.5 cm
0.1 cm
0.1 cm
1 m

## Slide 3: Submission
Will upload four input and four output files
  “1D” SS, “1-D” transient, 2-D SS, 2-D transient
Will upload a written report, 5-10 pages (including figures), times new roman, 12pt, 1.5 space
Due April 30 (last day of classes)
This is an individual project, but some collaboration is encouraged