## Slide 1: MOOSE Project
Three-part project
Will upload input and output files to Moodle
Will upload a written Part 1 report, max of 10 pages (including figures)
This is an individual project, but some collaboration is encouraged
Write up with deliverables from Part 1, choice of materials, mesh, details therein, etc.
Part 1 is due March 3

## Slide 2: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Outer cladding temperature is constant: 600 K
Solve temperature profile for:
  Steady-state: Q = 350 W/cm^3
  Compare against analytical solution
Use both a constant k and a temperature-dependent k
Perform a mesh convergence study
Use transient solver
Explore two mesh options:
  explicitly meshing the gap
  without meshing the gap
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 cm