## Slide 1: MOOSE Project
Fuel pin dimensions listed
Fuel thermal conductivity: 0.3 W/cm-K
Cladding thermal conductivity: 0.17 W/cm-K
Gap thermal conductivity: 0.1 W/cm-K
Outer cladding: 500 K
Mesh: 100x100
Solve temperature profile for:
  Steady-state: Volumetric/Areal heating rate: Q = 250 W/cm2
Solve for centerline temperature vs time
  Transient: Volumetric/Areal heating rate: Q = 150*EXP(-0.03*time)+250, for up to t=200
Will submit input files, output files, and your results in powerpoint
Fuel
Gap
Cladding
0.5 cm
0.1 cm
0.1 cm
1 cm