## Slide 1: MOOSE Project
Three-part project
Will upload input and output files to Moodle
Will upload a final written report, max of 10 pages (including figures), times new roman, 12pt, 1.5 space, pdf
Due April 23 – last day of classes
This is an individual project, but some collaboration is encouraged

## Slide 2: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Outer cladding temperature: 550 K
Solve temperature profile for:
  Steady-state: LHR = 350 W/cm2
  Compare against analytical solution
Solve for centerline temperature vs time
  Transient: LHR = 250*EXP(-((B3-20)^2)/10)+150
  for up to t=100
Use both a constant k and a temperature-dependent k
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 cm

## Slide 3: Part 1 Writeup
Will upload input and output files to Moodle
Write up with deliverables from Part 1, choice of materials, mesh, details therein, etc.
Part 1 writeup max of 5 pages

## Slide 4: MOOSE Project Part 2
Fuel pin dimensions listed – 2D RZ
Assume reasonable values for thermal conductivities, constant
Utilize axial Tcool, with Tcoolin= 500 K, reasonable flow rate, heat capacity, etc.
Utilize axial LHR, with LHR0=350 W/cm
Solve temperature profile for:
  z=0.25, z=0.5, z=1
Find axial location of peak centerline temperature at steady-state
Solve for centerline temperature vs time
  Transient: LHR0 = 250*EXP(-((B3-20)^2)/10)+150
  z=0.25, z=0.5, z=1
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 m

## Slide 5: Part 2 Writeup
Will upload input and output files to Moodle
Write up with deliverables from Part 1 & 2, choice of materials, mesh, details therein, etc.
Expected to have fixed any issues with Part 1
Part 2 writeup max of 8 pages

## Slide 6: MOOSE Project Part 3
Utilizing the system from Part 2, combine heat conduction and tensor mechanics in a fully thermo-mechanical simulation to get the stresses due to thermal expansion and irradiation-induced swelling in the fuel. Use thermo-mechanical contact to look at Pellet-Cladding Mechanical Interaction (PCMI) behaviors.
1) Assume a temperature dependent thermal conductivity from part 2
2) Assume an irradiation-induced swelling model (i.e., eigenstrain)
Can reduce boundary conditions to a fuel surface temp
Constant, axially varying, LHR
Only steady-state

## Slide 7: Part 3 Writeup
Will upload input and output files to Moodle
Write up with deliverables from Part 1 & 2 & 3, choice of materials, mesh, details therein, etc.
Expected to have fixed any issues with Part 1 and Part 2
Part 3 writeup max of 10 pages