## Slide 1: Final Project
Yuqing Huang
NE 591
Dr. Benjamin Beeler

## Slide 2: Introduction
Heat is produced in the fuel, transports through the cladding and gap, and into cladding
Heat transported through the fuel, cladding by conduction
Mostly heat transported through the gap by conduction, some by convection
Heat transported through coolant by convection

## Slide 3: Heat conduction
Heat conduction equation
  k is thermal conductivity
  is volumetric heating rate
  is density
  is specific heat capacity

## Slide 4: Heat Conduction in Light Water Reactor
Assumption
  Steady state heat conduction
  heat conduction is predominately in the radial direction
  Constant thermal conductivity
Boundary
  Symmetry
  conservation of heat flux at the fuel/gap/clad interface

## Slide 5: Heat Conduction in Light Water Reactor
Fuel region
Gap region
  is gap conductance;
  is fuel pellet surface temperature
  is inner clad surface temperature

## Slide 6: Heat Conduction in Light Water Reactor
Gap region
Cladding region

## Slide 7: Simulation Details
Outer cladding: 500 K
Mesh: 100x100
Steady-state: Volumetric/Areal heating rate: Q = 250 W/cm2 Transient: Volumetric/Areal heating rate: W/cm2 up to t=200
Fuel
Gap
Cladding
0.5 cm
0.1 cm
0.1 cm
1 cm

## Slide 8: Parameters for Materials
type | Thermal conductivity (W/cm-K) | Density(g/cm3) | Specific heat capacity(J/g-K)
Fuel | 0.3 | 10.98 | 0.33
Gap | 0.1 | 5.9 | 0.158
Cladding | 0.17 | 6.5 | 0.35

## Slide 9: Steady State
Volumetric/Areal heating rate: Q = 250 W/cm2
Heat conduction function for fuel
Heat conduction function for cladding/gap

## Slide 10: The Result for Steady State
These two figure are represented the temperature changes across the fuel, gap and cladding
There is parabolic temperature profile in fuel
Approximately Linear temperature profile in gap and clad
Lower thermal conductivity, steeper temperature drops. There is a steeper temperature drops in the gap

## Slide 11: Verification
Blue line is calculated by MATLAB through the analytical equation with heat transfer across the gap by equation
Yellow line is calculated by MATLAB through the analytical equation with heat transfer across the gap by equation
Red line is the moose result

## Slide 12: Transient
Volumetric/Areal heating rate: W/cm2, for up to t=200
Heat conduction function for fuel
Heat conduction function for cladding/gap
Assume the initial temperature for the system is 0K

## Slide 13: The Result for Transient
The animation for the temperature change cross the fuel, gap and cladding with time

## Slide 14: The Result for Transient
At beginning, The fuel heats up, the centerline temperature rapidly increase
As the time goes, the volumetric/areal heating rate decrease, thus the temperature will decrease.

## Slide 15: Conclusion
Moose can be used to solve heat equation at 1D steady state situation
The result for 1D steady state is same compared with analytical calculation
Moose can also work well for 1D transition