## Slide 1: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Outer cladding temperature: 550 K
Solve temperature profile for:
  Steady-state: LHR = 350 W/cm2
  Compare against analytical solution
Solve for centerline temperature vs time
  Transient: LHR = 250*EXP(-((t-20)^2)/10)+150
  for up to t=100
Use both a constant k and a temperature-dependent k
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 cm

## Slide 2: Part 1 Writeup
Will upload input and output files to Moodle
Write up with deliverables from Part 1, choice of materials, mesh, details therein, etc.
Part 1 writeup max of 5 pages
Due March 1, 11:59pm