## Slide 1: REVIEW OF LITERATURE ON MPM-FAST MODEL

## Slide 2: TABLE OF CONTENTS
INTRODUCTION
WHAT THE LITERATURE IS ABOUT
WHY THE LITERATURE?
LITERATURE FINDINGS
OUR FINDINGS AND THE WAY FORWARD
CONCLUSION

## Slide 3: INTRODUCTION
PAPER ADDRESSES THE UTILIZATION OF FIRST-OF-A-KIND MODEL
01
PAPER DOES NOT TRY TO ANALYZE THE FINDINGS OF THE EXPERIMENTS BUT THE VALIDITY OF THE MODEL USED.
02
MODEL DEVELOPED BY THE CANADIANS – YES, THEY BEAT US TO IT!
03
Notes: The paper titled “ A Thoria and Thorium Uranium Dioxide Nuclear Fuel Performance Model Prototype and Knowledge Gap Assessment” by J. S. Bell, et al, and published in The Journal of Nuclear Engineering and Radiation Science, Volume 5 in January 2019, assesses the validity and accuracy of a novel model, developed to better understand thorium based fuels in their application as a substitute to uranium based fuels in the nuclear industry; and not the accuracy of the results of the model in themselves.
The said model was developed by the Royal Canadian Military College, and incorporated variables to an already proven model – The Fuel and Sheath modelling tool (FAST), reliably used to analyze the nature of uranium based fuels, chiefly uranium dioxide, to determine key features of the thorium based fuels.

## Slide 4: WHAT EXACTLY - FOR TIME IS MONEY
EXACT NATURE OF THE MODEL – STRUCTURE AND FUNCTIONS WERE ANALYZED.
ASSUMPTIONS USED BY THE MODEL WERE ASSESSED
NATURE AND CREDIBILITY OF CHOSEN REFERENCE WAS EXPLAINED
Notes: The incorporation of variables specific to thorium based fuels – Thoria, Thorium Uranium dioxide, and Thorium Plutonium dioxide into the FAST model, resulted in the Multi Pellet Material Fast Model (MPM-FAST). The model analyzed the said fuels, principally in regards to fuel performance and fuel deformation. The collated data was then compared with established data about these features derived from post irradiation examination data from demountable element-221 (DME 221) fuel, collated by the Canadian Nuclear Laboratories.
Thermal-Physical properties and known irradiation properties of thorium-based fuels were added to the FAST model. Consequently, assumptions were made. Assumptions made included axial symmetry of the cylindrical fuel element, consequently reducing the model to a two-dimensional model; irradiation behavior of one pellet was considered a representation of all pellets within the fuel element; assumption that the bottom pellet and sheath were fixed in axial direction; and finally, the resulting geometry utilized by the model was assumed to be that of a half-sized pellet with corresponding section of the sheath with azimuthal symmetry and periodic boundary conditions applied.
The model was further assumed to functionally among other things, track the volume and composition of formed fission gases; determine internal void changes leading to pellet and sheath deformation during irradiation, determine internal pressures of pellets, determine heat transport within the pellet meshes and associated thermal conductivity, and finally, assumed to determine the burn-up variable – used as a measure of the fraction of initial heavy element atoms that took part in the fission process.
Three resulting variables assessed by the model were taken into account – the model’s assessment of fission gas release, center-line temperature, and end-of-life sheath strain.

## Slide 5: SO, WHY BOTHER?
SIMPLE! - THORIUM BASED FUELS HAVE LONG SHOWN MORE FAVORABLE CHARACTERISTICS.
Notes: Though adjudged to have among other things, better thermal conductivity, oxidation resistance, and higher melting pressure, thorium based fuels account for less than 1 percent of all industrial reactors. One reason has been the paucity of mechanisms to better understand them – as we do uranium based fuels, under working/industrial conditions.
The development of a model(s) that does this, opens a way to their better characterization, understanding and subsequent application - not necessarily as a replacement to uranium based fuels, but at least, as a viable alternative.

## Slide 6: RESULTS AND FINDINGS
CENTRE-LINE TEMPERATURE ASSESSMENT WAS POOR
FISSION GAS RELEASE ASSESMENT WAS INCONCLUSIVE
MODEL OVER PREDICTED THE END OF LIFE SHEATH STRAIN
Notes: The literature concluded that the model’s assessment of the center-line temperature was inaccurate, that of the fission gas release was inconclusive as only one of the two cases in the experimental process gave a good approximation of the fission gas released; and finally, the model over-predicted the fuel’s end-life sheath strain.

## Slide 7: CONCLUSION AND WHAT NEXT
UP UP UP CAN ONLY GO UP FROM HERE – SHANIA TWAIN!
MORE VARIABLES TO BE INCORPORATED
MORE REALIATIC ASSUMPTIONS TO BE MADE
WHATEVER HAPPENS, DON’T STOP THE MUSIC!
Notes: The view of thorium based fuels as the nuclear holy grail has long been present, going on decades now. Even with a score of “half” out of three, looking at the glass as half full instead of half empty is the way to go.
More realistic assumptions regarding the symmetry/geometry of the pellets and a three-dimensional model approach should be entertained among other things to make the model more accurate and valid.
Equally, more variables such as rate of oxidation can be included in the model to give a view of not only performance and deformation, but also durability and the ability to react well in times of disaster.