## Slide 1: Fuel Performance
NE 591

## Slide 2: Last Time
Developed analytical solutions for temperature profile
This time, we move from the analytical into the numerical framework
Parabolic profile of temperature in fuel
Cosine profile of LHR as a function of z on fuel rod

## Slide 3: Review of Assumptions
Analytical solution requires:
  Steady-state solution
  Temperature is axisymmetric
  T is constant in Z
  Thermal conductivity is independent of temperature
  Temperature profile in the fuel is parabolic, linear profiles in gap, clad and coolant

## Slide 4: Clarifications
Heat flux is a conserved quantity, described by Fourier’s first and second laws:
If there are no sources of heat, as if the case in the cladding and gap, the temperature field is constant with time and heat flux is unidirectional
l = thermal cond.

## Slide 5: Clarifications
For boundary conditions T1 and T2 and a thickness d:
This assumes a spatially constant thermal conductivity
Our thin slab assumption sets the thermal conductivity to a single value in the gap and cladding
We know that thermal conductivity is a function of temperature

## Slide 6: Numerical time integration

## Slide 7: For numerical solutions, deal with derivatives in space/time
Derivatives in time
  Forward Euler’s method (explicit)
  Backward Euler’s method (implicit)
Derivatives in space
  Finite difference
  Finite volume
  Finite element

## Slide 8: Forward Euler
Step forward through time in increments, dt
The Euler method is a first-order method, which means that the local error (error per step) is proportional to the square of the step size
Expand a function y(t), with a timestep size, h
Euler takes only the first derivative
Value yn is an approximation of the solution to the ODE at time tn

## Slide 9: Forward Euler
Applying to our temperature system
Using the heat conduction equation:
We input T0, which here is T @ t=0, step size dt
  Tn+1 = Tn + dt*T’; tn+1 = tn + dt
t
T

## Slide 10: Backwards Euler
Backwards Euler for a function T(r,t)
This differs from Forward Euler in that here we use (r,t+dt), instead of (r,t)
Tn+1 = Tn + dt T’(r,t+dt), tn+1 = tn + dt
The new approximation appears on both sides of the equation, thus this method needs to solve an algebraic equation for the unknown future state
This can be done with fixed-point iteration or non-linear solvers
Improved Euler is a form of explicit Euler (explicit trapezoidal rule), which takes the derivative at the midpoint
t

## Slide 11: Explicit vs Implicit
Forward Euler is explicit
  Explicit methods calculate the state of a system at a later time from the state of the system at the current time
  Can be unstable if step size is too much
Backwards Euler is implicit
  Implicit methods find a solution by solving an equation involving both the current state of the system and a later state
  Implicit require an extra computation and they can be much harder to implement
  Implicit methods are used because many problems arising in practice are stiff, for which the use of an explicit method requires very small timesteps

## Slide 12: Example Problem

## Slide 13: Spatial discretization

## Slide 14: Spatial resolution
To numerically solve in space, we need to discretize
  Finite difference
    convert differential equations into a system of equations that can be solved by matrix algebra techniques
  Finite volume
    volume integrals in a partial differential equation that contain a divergence term are converted to surface integrals, using the divergence theorem. These terms are then evaluated as fluxes at the surfaces of each finite volume
  Finite element
    subdivides a large system into smaller, simpler parts that are called finite elements, the equations that model these finite elements are then assembled into a larger system of equations that models the entire problem

## Slide 15: Finite Difference
The finite difference method solves on a grid and uses numerical derivatives
Derivatives are approximated by differences
Boundary conditions must have either a fixed T or dT/dr
Typically restricted to handle rectangular shapes
Once you compute the time derivative, you can use either forward or backward Euler to march through time
T(r – h, t)
T(r + h, t)
T(r, t)

## Slide 16: Finite Volume
Discretize the domain by subdomains
  Domain size h
  We place points in the subdomain centers and on either boundary
The finite volume method balances fluxes across the boundaries of your divided subdomains
Integrate our PDE across the subdomain
Evaluate the integral using a linear approximation of the variable
Restricted to flux boundary conditions, often used in flow-type problems

## Slide 17: Finite Element
In the finite element method, we interpolate the variable using nodal values and integrate over elements
Systematically recombine all sets of element equations into a global system of equations for the final calculation
Write the strong form of the equation, rearrange to get zero on the right-hand side, multiply by the test function, integrate over the domain, yielding weak form
The strong form states conditions that must be met at every material point, whereas weak form states conditions that must be met only in an average sense
Finite element works for any geometry and any boundary condition
e1
e2
e3
n1 n2 n3 n4

## Slide 18: Spatial resolution
Finite difference
  Advantages
    Simple
    Easy to code
    Fast
  Disadvantages
    Difficult to model complex geometries
    Difficult to model complex BCs
    Only represents solution at points
    Difficult to represent heterogeneous properties
Finite Element
  Advantages
    Can model any geometry
    Can model any BC
    Continuous representation
    Heterogeneous properties
  Disadvantages
    Complicated
    Somewhat more expensive
Finite Volume
  Advantages
    Can model any geometry
    Naturally conservative
    Heterogeneous properties
  Disadvantages
    Boundary conditions add complexity
    More complicated than finite difference

## Slide 19: Different Fuel Performance Problems
Computational cost
Accuracy
Transient, full 3D
Transient, 2D axisymmetric with discrete pellets
Transient, 2D axisymmetric with smeared pellets
Transient, multiple 1D slices (1.5D)
Transient, 1D
Steady state, 1D (analytical)

## Slide 20: Numerical Approaches to Different Fuel Performance Problems
Computational cost
Accuracy
Transient, full 3D
FEM or FV
Transient, 2D axisymmetric with discrete pellets
FEM or FV
Transient, 2D axisymmetric with smeared pellets
FEM, FV, or FD
Transient, multiple 1D slices (1.5D)
FEM, FV, or FD
Transient, 1D
FEM, FV, or FD
Steady state, 1D (analytical)

## Slide 21: Heat equation solution approach summary
Approach | Solution | Assumptions
1D steady state | Analytical | Steady state, axisymmetric, no axial variation, constant k
1D transient | FEM, FD, FV | Axisymmetric, no axial variation
1.5D transient | FEM, FD, FV with multiple slices | Axisymmetric, no axial variation
2D transient, smeared pellets | FEM, FD, FV | Axisymmetric, fuel pellets act as one body, fuel pellets are perfect cylinders
2D transient, discrete pellets | FEM, FV | Axisymmetric
3D transient | FEM, FV | You have a big computer
Each numerical solution can be solved explicitly or implicitly

## Slide 22: Solving with fuel performance codes
Fuel performance codes primarily use either finite difference or finite element
The earliest fuel performance codes solved the heat equation in 1.5D using finite difference (with multiple axial slices)
More modern codes have switched to finite element, due to more flexibility with geometry and boundary conditions
Finite volume is not used because it can’t solve for the stress

## Slide 23: Summary
The heat equation can be solved using numerical methods.
Spatial derivative solution methods divide the domain up into smaller pieces
  Finite difference
  Finite volume
  Finite element
Each discretization has strengths/weaknesses
Finite element is primary method for high fidelity fuel performance codes

## Slide 24: Notes
Exam on Feb. 3
Will cover all classes through this Thursday
Will contain both conceptual and work-through problems
Major topics covered:
  Fuel types; Heat generation; Reactor Systems; Fuel fabrication; Heat transfer; Analytical solution to heat transfer; Numerical solution to heat transfer; Thermal conductivity; Operational Limits
In-person: during class time
Online: total of 1.5 hours to complete the exam (class period plus 15-minute buffer)
Distance students: please schedule your exam with me, otherwise it will be assumed you will be completing it during class time
In person students: Option to complete in person during class, or online during the class period
Next time will be partial lecture and partial problem session

## Slide 25: Time Integration From Class
t | y' |  | forward | backward |  | function
1 | 1 |  | 6 | 6 |  | 6
1.333333 | 1.3333E-06 |  | 6.333333 | 6.00000044 |  | 6.18518519
1.666666 | -1.6666627 |  | 6.33333344 | 5.44444678 |  | 5.92592704
1.999999 | -3.999992 |  | 5.77777978 | 4.11111744 |  | 5.000004
2.333332 | -6.9999867 |  | 4.44445044 | 1.77779089 |  | 3.18519452
2.666665 | -10.666647 |  | 2.11112389 | -1.7777544 |  | 0.25927704
2.999998 | -14.999972 |  | -1.4444214 | -6.7777401 |  | -3.99997
3.333331 | -19.999963 |  | -6.4444071 | -13.444388 |  | -9.8147681
3.666664 | -25.666619 |  | -13.111055 | -21.999919 |  | -17.407339
Chart: 
| 1 | 1.3333330000000001 | 1.6666660000000002 | 1.9999990000000003 | 2.3333320000000004 | 2.6666650000000005 | 2.9999980000000006 | 3.3333310000000007 | 3.6666640000000008
Function | 6 | 6.1852 | 5.9259 | 5 | 3.1852 | 0.25928 | -4 | -9.8148 | -17.4073
Forward | 6 | 6.3333 | 6.3333 | 5.7778 | 4.4445 | 2.1111 | -1.4444 | -6.4444 | -13.1111
Backward | 6 | 6 | 5.4444 | 4.1111 | 1.7778 | -1.7778 | -6.7777 | -13.4444 | -21.9999