## Slide 1: Fuel Performance
NE 533: Spring 2023

## Slide 2: Last Time
Had an exam…
Any feedback?

## Slide 3: MOOSE Project
Three-part project
Will upload input and output files to Moodle
Will upload a final written report, 5-10 pages (including figures), times new roman, 12pt, 1.5 space, pdf
Final report is due April 21 – Friday last week of classes
This is an individual project, but some collaboration is encouraged
Part 1 is due Feb 24
  just input/output submitted to moodle; 1 page report outlining results
  don’t wait until the last minute to do this! ask questions

## Slide 4: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Can assume constant k
Outer cladding temperature: 600 K
Mesh: something sufficiently converged
Solve temperature profile for:
  Steady-state: LHR = 350 W/cm2
  Compare against analytical solution
Solve for centerline temperature vs time
  Transient: LHR = 500*[(t/100)^0.5]*[(1-(t/100))^4] + 150
  for up to t=100
Fuel
Gap
Cladding
0.5 cm
0.002 cm
0.1 cm
1 cm

## Slide 5: The most accurate solution is numerical, in 3D, requires modeling the entire core, and is multi-physics
Solution is 3D and changes in time
All the properties are functions of temperature
The boundary conditions comes from information about the coolant flow
The heat generation rate comes from information about the neutronics in the reactor
No analytical solution is possible

## Slide 6: Numerical time integration

## Slide 7: For numerical solutions, deal with discretization in space/time
Discretization in time
  Forward Euler’s method (explicit)
  Backward Euler’s method (implicit)
Discretization in space
  Finite difference
  Finite volume
  Finite element

## Slide 8: Forward Euler
Step forward through time in increments, dt
The Euler method is a first-order method, which means that the local error (error per step) is proportional to the square of the step size
Expand a function y(t), with a timestep size, h
Euler takes only the first derivative
Value yn is an approximation of the solution to the ODE at time tn

## Slide 9: Forward Euler
Applying to our temperature system
Using the heat conduction equation:
We input T0, which here is T @ t=0, step size dt
  Tn+1 = Tn + dt*T’; tn+1 = tn + dt
t
T

## Slide 10: Backwards Euler
Backwards Euler for a function T(r,t)
This differs from Forward Euler in that here we use (r,t+dt), instead of (r,t)
Tn+1 = Tn + dt T’(r,t+dt), tn+1 = tn + dt
The new approximation appears on both sides of the equation, thus this method needs to solve an algebraic equation for the unknown future state
This can be done with fixed-point iteration or non-linear solvers
Improved Euler is a form of explicit Euler (explicit trapezoidal rule), which takes the derivative at the midpoint
t

## Slide 11: Explicit vs Implicit
Forward Euler is explicit
  Explicit methods calculate the state of a system at a later time from the state of the system at the current time
  Can be unstable if step size is too much
Backwards Euler is implicit
  Implicit methods find a solution by solving an equation involving both the current state of the system and a later state
  Implicit require an extra computation and they can be much harder to implement
  Implicit methods are used because many problems arising in practice are stiff, for which the use of an explicit method requires very small timesteps

## Slide 12: Stiff Equations
A stiff equation is a differential equation for which certain numerical methods for solving the equation are numerically unstable, unless the step size is taken to be extremely small
Consider the problem:
Where the exact solution is:
Euler's method with a step size of ℎ=1/4 oscillates wildly
Euler's method with half the step size, ℎ=/18, produces a solution within the graph boundaries, but oscillates about zero
The trapezoidal method (similar to backwards Euler) is implicit, and converges to the correct solution

## Slide 13: Example Problem

## Slide 14: Example Problem
y’=t*exp(-2t)
y0=4
dt=0.5
Backwards Euler

## Slide 15: Spatial discretization

## Slide 16: Spatial resolution
To numerically solve in space, we need to discretize
  Finite difference
    convert differential equations into a system of equations that can be solved by matrix algebra techniques
  Finite volume
    volume integrals in a partial differential equation that contain a divergence term are converted to surface integrals, using the divergence theorem. These terms are then evaluated as fluxes at the surfaces of each finite volume
  Finite element
    subdivides a large system into smaller, simpler parts that are called finite elements, the equations that model these finite elements are then assembled into a larger system of equations that models the entire problem

## Slide 17: Finite Difference
The finite difference method solves on a grid and uses numerical derivatives
Derivatives are approximated by differences
Boundary conditions must have either a fixed T or dT/dr
Typically restricted to handle rectangular shapes
Once you compute the time derivative, you can use either forward or backward Euler to march through time
T(r – h, t)
T(r + h, t)
T(r, t)

## Slide 18: Finite Volume
Discretize the domain by subdomains
  Domain size h
  We place points in the subdomain centers and on either boundary
The finite volume method balances fluxes across the boundaries of your divided subdomains
Integrate our PDE across the subdomain
Evaluate the integral using a linear approximation of the variable
Restricted to flux boundary conditions, often used in flow-type problems

## Slide 19: Finite Element
In the finite element method, we interpolate the variable using nodal values and integrate over elements
Systematically recombine all sets of element equations into a global system of equations for the final calculation
Write the strong form of the equation, rearrange to get zero on the right-hand side, multiply by the test function, integrate over the domain, yielding weak form
The strong form states conditions that must be met at every material point, whereas weak form states conditions that must be met only in an average sense
Finite element works for any geometry and any boundary condition
e1
e2
e3
n1 n2 n3 n4

## Slide 20: Spatial resolution
Finite difference
  Advantages
    Simple
    Easy to code
    Fast
  Disadvantages
    Difficult to model complex geometries
    Difficult to model complex BCs
    Only represents solution at points
    Difficult to represent heterogeneous properties
Finite Element
  Advantages
    Can model any geometry
    Can model any BC
    Continuous representation
    Heterogeneous properties
  Disadvantages
    Complicated
    Somewhat more expensive
Finite Volume
  Advantages
    Can model any geometry
    Naturally conservative
    Heterogeneous properties
  Disadvantages
    Boundary conditions add complexity
    More complicated than finite difference

## Slide 21: Different Fuel Performance Problems
Computational cost
Accuracy
Transient, full 3D
Transient, 2D axisymmetric with discrete pellets
Transient, 2D axisymmetric with smeared pellets
Transient, multiple 1D slices (1.5D)
Transient, 1D
Steady state, 1D (analytical)

## Slide 22: Numerical Approaches to Different Fuel Performance Problems
Computational cost
Accuracy
Transient, full 3D
FEM or FV
Transient, 2D axisymmetric with discrete pellets
FEM or FV
Transient, 2D axisymmetric with smeared pellets
FEM, FV, or FD
Transient, multiple 1D slices (1.5D)
FEM, FV, or FD
Transient, 1D
FEM, FV, or FD
Steady state, 1D (analytical)

## Slide 23: Heat equation solution approach summary
Approach | Solution | Assumptions
1D steady state | Analytical | Steady state, axisymmetric, no axial variation, constant k
1D transient | FEM, FD, FV | Axisymmetric, no axial variation
1.5D transient | FEM, FD, FV with multiple slices | Axisymmetric, no axial variation
2D transient, smeared pellets | FEM, FD, FV | Axisymmetric, fuel pellets act as one body, fuel pellets are perfect cylinders
2D transient, discrete pellets | FEM, FV | Axisymmetric
3D transient | FEM, FV | You have a big computer
Each numerical solution can be solved explicitly or implicitly

## Slide 24: Solving with fuel performance codes
Fuel performance codes primarily use either finite difference or finite element
The earliest fuel performance codes solved the heat equation in 1.5D using finite difference (with multiple axial slices)
More modern codes have switched to finite element, due to more flexibility with geometry and boundary conditions
Finite volume is becoming an option

## Slide 25: Summary
The heat equation can be solved using numerical methods.
Spatial derivative solution methods divide the domain up into smaller pieces
  Finite difference
  Finite volume
  Finite element
Each discretization has strengths/weaknesses
Finite element is primary method for high fidelity fuel performance codes

## Slide 26: Mechanics

## Slide 27: Solid mechanics
When a load is applied to a body, it changes shape and perhaps size
Motions throughout a body are called displacements
  u(r, t)
Rigid body displacements do not change the shape and/or size
  the rigid body is translated
Changes in shape and/or size are call deformations
The objective of Solid Mechanics is to relate loads (applied force) to deformation

## Slide 28: Ideal springs
It can be instructive to view solids as a spring
When we apply some force F, we get some displacement x
  F = k x
When the spring is displaced by x, there is force that responds in the opposite direction equal to kx
Due to the displacement, there is a stored energy E = ½ k x2

## Slide 29: Observed deformation due to a force
Solid mechanics is similar to the behavior of an ideal spring but throughout a body
An applied load results results in deformation.
The internal strain is like the displacements x
The internal stress is like the internal force F

## Slide 30: Elasticity
Elasticity is the ability of a body to resist a distorting influence and to return to its original size and shape when that influence or force is removed
In elastic deformation, we are stretching the atomic bonds
The more we stretch the bonds, the more force it takes to stretch
When we release the load, the atoms spring back into their lattice sites