## Slide 1: Heat Transport
NE 591

## Slide 2: Last Time
Developed analytical solutions for temperature profile
This time, we move from the analytical into the numerical framework

## Slide 3: Review of Assumptions
Analytical solution required:
  Steady-state solution
  Temperature is axisymmetric
  T is constant in Z
  Thermal conductivity is independent of temperature
  Temperature profile in the fuel is parabolic, linear profiles in gap, clad and coolant
For now, numerical solution we will assume:
  Axisymmetric
  Constant in Z

## Slide 4: Simplify our heat conduction equation
Start with heat conduction equation
Assume axisymmetric (2D-rz)
Assume constant in z
This equation cannot
be solved analytically

## Slide 5: For numerical solutions, deal with derivatives in space/time
Derivatives in time
  Forward Euler’s method (explicit)
  Backward Euler’s method (implicit)
Derivatives in space
  Finite difference
  Finite volume
  Finite element

## Slide 6: Forward Euler
Step forward through time in increments, dt
The Euler method is a first-order method, which means that the local error (error per step) is proportional to the square of the step size
Expand a function y(t), with a timestep size, h
Euler takes only the first derivative
Value yn is an approximation of the solution to the ODE at time tn

## Slide 7: Forward Euler
Applying to our temperature system
Using the heat conduction equation:
We input T0, which here is T @ t=0, step size dt
  Tn+1 = Tn + dt*T’; tn+1 = tn + dt
t
T

## Slide 8: Backwards Euler
Backwards Euler for a function T(r,t)
This differs from Forward Euler in that here we use (r,t+dt), instead of (r,t)
T(0) = T0; t1 = t0 + dt
Tn+1 = Tn + dt T’(r,t+dt)
Improved Euler is a form of explicit Euler (explicit trapezoidal rule)
t
T

## Slide 9: Explicit vs Implicit
Forward Euler is explicit
  Explicit methods calculate the state of a system at a later time from the state of the system at the current time
  Can be unstable if step size is too much
Backwards Euler is implicit
  Implicit methods find a solution by solving an equation involving both the current state of the system and a later state
  Implicit require an extra computation and they can be much harder to implement
  Implicit methods are used because many problems arising in practice are stiff, for which the use of an explicit method requires very small timesteps

## Slide 10: Spatial resolution
To numerically solve in space, we need to discretize
  Finite difference
    convert differential equations into a system of equations that can be solved by matrix algebra techniques
  Finite volume
    volume integrals in a partial differential equation that contain a divergence term are converted to surface integrals, using the divergence theorem. These terms are then evaluated as fluxes at the surfaces of each finite volume
  Finite element
    subdivides a large system into smaller, simpler parts that are called finite elements, the equations that model these finite elements are then assembled into a larger system of equations that models the entire problem

## Slide 11: Spatial resolution
Finite difference:
  Advantages
    Simple
    Easy to code
  Disadvantages
    Difficult to model complex geometries
    Difficult to model complex BCs
    Only represents solution at points
    Difficult to represent heterogeneous properties
    No guarantee of convergence