## Slide 1: MOOSE Project
Three-part project
Will upload input and output files to Moodle
Will upload a final written report, 5-10 pages (including figures), times new roman, 12pt, 1.5 space, pdf
Due April 21 – Friday last week of classes
This is an individual project, but some collaboration is encouraged
Part 1 is due Feb 24
  just input/output submitted to moodle; 1 page report outlining results

## Slide 2: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Can assume constant k
Outer cladding temperature: 600 K
Mesh: something sufficiently converged
Solve temperature profile for:
  Steady-state: LHR = 350 W/cm2
  Compare against analytical solution
Solve for centerline temperature vs time
  Transient: LHR = 500*[(t/100)^0.5]*[(1-(t/100))^4] + 150
  for up to t=100
Fuel
Gap
Cladding
0.5 cm
0.002 cm
0.1 cm
1 cm