## Slide 1: MOOSE Project
Three-part project
Will upload input and output files to Moodle
Will upload a written report, max of 10 pages (including figures)
This is an individual project, but some collaboration is encouraged
Write up with deliverables from Part 1, choice of materials, mesh, details therein, etc.
Part 1 is due Feb. 28

## Slide 2: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Outer cladding temperature is constant: 550 K
Solve temperature profile for:
  Steady-state: LHR = 350 W/cm2
  Compare against analytical solution
Solve for centerline temperature vs time
  Transient: LHR = 350*EXP(-((t-20)^2)/2)+350
  for up to t=100
  Get peak T value
Use both a constant k and a temperature-dependent k
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 cm