## Slide 1: MOOSE Project Part 2
Fuel pin dimensions listed – 2D RZ
Assume reasonable values for thermal conductivities, constant
Utilize axial Tcool, with Tcoolin= 500 K, reasonable flow rate, heat capacity, etc.
Utilize axial LHR, with LHR0=350 W/cm
Solve temperature profile for:
  @ z=0.25, z=0.5, z=1
Solve for centerline temperature vs time
  Transient: LHR0 = 500*[(t/100)^0.5]*[(1-(t/100))^4] + 150
  @ z=0.25, z=0.5, z=1
Find location of peak centerline temperature at steady-state and at t=100 in transient
Fuel
Gap
Cladding
0.5 cm
0.002 cm
0.1 cm
1 m