## Slide 1: MOOSE Project
Three-part project
Will upload input and output files to Moodle
Will upload a final written report, max of 10 pages (including figures), times new roman, 12pt, 1.5 space, pdf
Due April 23 – last day of classes
This is an individual project, but some collaboration is encouraged

## Slide 2: MOOSE Project Part 1
Fuel pellet dimensions listed
This is a 1-D problem, but I want your geometry to be set up in 2-D RZ
Assume reasonable values for material properties
Can assume constant k
Outer cladding temperature: 600 K
Mesh: something sufficiently converged
Solve temperature profile for:
  Steady-state: LHR = 350 W/cm2
  Compare against analytical solution
Solve for centerline temperature vs time
  Transient: LHR = 500*[(t/100)^0.5]*[(1-(t/100))^4] + 150
  for up to t=100
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 cm

## Slide 3: MOOSE Project Part 2
Fuel pin dimensions listed – 2D RZ
Assume reasonable values for thermal conductivities, constant
Utilize axial Tcool, with Tcoolin= 500 K, reasonable flow rate, heat capacity, etc.
Utilize axial LHR, with LHR0=350 W/cm
Solve temperature profile for:
  @ z=0.25, z=0.5, z=1
Solve for centerline temperature vs time
  Transient: LHR0 = 500*[(t/100)^0.5]*[(1-(t/100))^4] + 150
  @ z=0.25, z=0.5, z=1
Find location of peak centerline temperature at steady-state and at t=100 in transient
Fuel
Gap
Cladding
0.5 cm
0.005 cm
0.1 cm
1 m

## Slide 4: MOOSE Project Part 3
Utilizing the system from Part 2, combine heat conduction and tensor mechanics in a fully thermo-mechanical simulation to get the stresses due to thermal expansion in the fuel
1) Assume a constant thermal conductivity
2) Assume a temperature dependent thermal conductivity
Can neglect any potential effects of contact, can reduce boundary conditions to a fuel surface temp
Constant, axially varying, LHR
Only steady-state